## Slide 1: Idealized Tropical Cyclone(TC) Simulation with FV3GFS
Jiayi Peng, Kate Zhou, Henry Juang, Sajal Kar
Jun Wang, Fanglin Yang, Xingren Wu, Dusan Jovic
HWRF Weekly Meeting on October 08, 2020

## Slide 2: /ufs-weather-model/FV3/atmos_cubed_sphere/tools/test_cases.F90
(I) test_case=-55 in West Pacific with TC center (10N;180E)
(II) test_case= 55 in West Pacific with TC center (10N;180E)
(III) test_case= 57 in West Pacific with TC center (10N;180E) and f-plane (Coriolis parameter is constant)
(IV) test_case=57a in West Pacific with TC center (10N; 180E), f-plane and aqua-planet
(V) test_case= 4a/b Two-vortices interaction in Atlantic (shallow water model)

## Slide 3
subroutine DCMIP16_TC ----- test_case=-55 (./FV3/atmos_cubed_sphere/tools/test_cases.F90)
real, parameter :: zt = 15000 !< m
real, parameter :: q0 = 0.021 !< kg/kg
real, parameter :: qt = 1.e-11 !< kg/kg
real, parameter :: T0 = 302.15 !< K
real, parameter :: Tv0 = 302.15*(1.+0.608*q0) !< K
real, parameter :: Ts = 302.15 !< K
real, parameter :: zq1 = 3000. !< m
real, parameter :: zq2 = 8000. !< m
real, parameter :: lapse = 7.e-3 !< K/m
real, parameter :: Tvt = Tv0 - lapse*zt !< K
real, parameter :: pb = 101500. !< Pa
real, parameter :: ptt = pb*(TvT/Tv0)**(grav/Rdgas/lapse)
real(kind=R_GRID), parameter :: lamp = pi
real(kind=R_GRID), parameter :: phip = pi/18.
real(kind=R_GRID), parameter :: ppcenter(2) = (/ lamp, phip /)
real, parameter :: dp = 1115. !< Pa
real, parameter :: rp = 282000. !< m
real, parameter :: zp = 7000. !< m
real, parameter :: fc = 2.*OMEGA*sin(phip)
real, parameter :: zconv = 1.e-6
!PS
do j=js,je
do i=is,ie
ps(i,j) = pb - dp*exp( -sqrt((rc(i,j)/rp)**3) )
enddo
enddo
zs=0 ….no orography
https://github.com/ClimateGlobalChange/DCMIP2016/blob/master/DCMIP2016-TestCaseDocument_v1.pdf
Jordan CL. Mean soundings for the west indies area. Journal of Meteorology 1958; 15(1):91–97.

## Slide 4
Initial TC in West Pacific (Test No.I /test_case=-55)
(Coriolis parameter is not constant)
pb=1015.0hPa, dp=11.15hPa, rp=282.0km
SLP: max=1015.00000000000 min=1004.44141134051
Surface wind:
U max = 19.4412681540063 min = -19.6647631637477
V max = 19.5408656635388 min = -19.8586152022006
Initial surface temperature /SST: 2016/10/03 00Z GFS analysis
Physics(fv3_ccpp_gfs_v15p2):
NSSTM is active (2, 1, 0, 0, 0)
scale & aerosol-aware mass-flux deep conv scheme
scale-aware hybrid edmf PBL scheme used
scale- & aerosol-aware mass-flux shallow conv scheme (2017)
Original mountain blocking and oragraphic gravity wave drag parameterization used
non-statioary gravity wave drag parameterization used ( do_gwd= T )
Radiative heating calculated at 64 layers
max-random cloud overlap for Shortwave IOVR_SW= 1
max-random cloud overlap for Longwave IOVR_LW= 1
sub-grid cloud for Shortwave ISUBC_SW= 2
sub-grid cloud for Longwave ISUBC_LW= 2
Using GFDL Cloud Microphysics
!PS
do j=js,je
do i=is,ie
ps(i,j) = pb - dp*exp( -sqrt((rc(i,j)/rp)**3) )
enddo
enddo

## Slide 5
TSEA in sfc_data.tile*.nc
2016/10/03 00Z GFS analysis
Land_sea_ice mask
SLMSK in sfc_data.tile*.nc

## Slide 6
@240 hrs
@120 hrs
@0.5 hrs
Test No.I /-55
Surface Pressure

## Slide 7
@240 hrs
@0.5 hrs
@120 hrs
Test No.I /-55
U at 10m

## Slide 8
@0.5 hrs
@120 hrs
@240 hrs
Test No.I /-55
V at 10m

## Slide 9
Test No.II /test_case= 55
(Coriolis parameter is not constant)
p00=1015.0hPa, dp=11.15hPa, rp=282.0km
The initial TC of Test No.II (test_case=55) is similar to Test No.I (test_case=-55), there may be some difference in thermal structure.
Surface pressure (PS) max=1015.00000000000 min=1004.44141134051
U max = 19.4412681540063 min = -19.6647631637477
V max = 19.5408656635388 min = -19.8586152022006
! Initialize surface Pressure
!Vortex perturbation
do j=js,je
do i=is,ie
p2(:) = agrid(i,j,1:2)
r = great_circle_dist( p0, p2, radius )
ps(i,j) = p00 - dp*exp(-(r/rp)**1.5)
phis(i,j) = 0.
enddo
enddo

## Slide 10
Test No.II/ 55
Surface Pressure
@0.5 hrs
@120 hrs
@240 hrs

## Slide 11
Test No.II/ 55
U at 10m
@0.5 hrs
@120 hrs
@240 hrs

## Slide 12
Test No.II/ 55
V at 10m
@0.5 hrs
@120 hrs
@240 hrs

## Slide 13: Test NO.I/II SLP forecast
Chart: Sea Level Pressure
| 0 | 6 | 12 | 18 | 24 | 30 | 36 | 42 | 48 | 54 | 60 | 66 | 72 | 78 | 84 | 90 | 96 | 102 | 108 | 114 | 120 | 126 | 132 | 138 | 144 | 150 | 156 | 162 | 168 | 174 | 180 | 186 | 192 | 198 | 204 | 210 | 216 | 222 | 228 | 234 | 240
TC-55 | 1004.4414 | 1005.1919 | 1004.1603 | 1002.5962 | 1005.1011 | 1004.4627 | 1005.3671 | 998.7986 | 994.2731 | 987.5242 | 988.4183 | 983.1458 | 978.7262 | 973.5652 | 975.8946 | 977.4044 | 969.6098 | 973.5159 | 972.8497 | 966.5686 | 965.1962 | 957.2634 | 964.2103 | 964.8489 | 958.7983 | 964.1752 | 961.7242 | 958.0749 | 955.4322 | 953.8 | 959.2296 | 956.6293 | 954.6439 | 953.1465 | 950.6622 | 952.8369 | 948.5154 | 947.1424 | 945.7142 | 944.8123 | 947.4932
TC+55 | 1004.4414 | 1005.1429 | 1005.0937 | 1002.6393 | 1004.6677 | 1004.0538 | 1003.4334 | 999.2344 | 993.2664 | 985.8968 | 991.9541 | 978.5649 | 979.0216 | 980.3782 | 980.1378 | 974.2096 | 980.69 | 976.569 | 979.9473 | 979.6101 | 973.6752 | 970.5428 | 966.6562 | 967.8594 | 958.7264 | 961.3048 | 962.1243 | 963.9994 | 961.2882 | 958.1613 | 963.494 | 960.2944 | 958.8444 | 955.0311 | 956.3388 | 954.2357 | 951.6987 | 949.3017 | 947.6413 | 944.899 | 945.5149
Forecast hours

## Slide 14
Test No.III (test_case= 57) on f-plane
(Coriolis parameter is constant)
p00=1015.0hPa, dp=11.15hPa, rp=282.0km
! Initialize surface Pressure
!Vortex perturbation
do j=js,je
do i=is,ie
p2(:) = agrid(i,j,1:2)
r = great_circle_dist( p0, p2, radius )
ps(i,j) = p00 - dp*exp(-(r/rp)**1.5)
phis(i,j) = 0.
enddo
enddo
Surface pressure (PS) max= 1015.00000000000 min=1004.44141134051
U max = 19.4412124264969 min = -19.6647077418568
V max = 19.5408117630522 min = -19.8585596483430

## Slide 15
Test No.III / 57
Surface Pressure
@0.5 hrs
@120 hrs
@240 hrs

## Slide 16
Test No.III / 57
U at 10m
@0.5 hrs
@120 hrs
@240 hrs

## Slide 17
Test No.III / 57
V at 10m
@0.5 hrs
@120 hrs
@240 hrs

## Slide 18
Test No.III / 57
Zonal wind (U)
Cross-section @180E
@120 hrs
South North

## Slide 19
@120 hrs
Test No.III / 57
Meridional wind (V)
Cross-section @12N
West East

## Slide 20
Test No.IV (test_case= 57a) on f-plane, aqua-planet
p00=1015.0hPa, dp=11.15hPa, rp=282.0km
Surface pressure (PS) max= 1015.00000000000 min=1004.44141134051
U max = 19.4412124264969 min = -19.6647077418568
V max = 19.5408117630522 min = -19.8585596483430
NSSTM is active (1, 1, 0, 0, 0)
!< nstf_name(1) : 0 = NSSTM off, 1 = NSSTM on but uncoupled
!< 2 = NSSTM on and coupled
!< nstf_name(2) : 1 = NSSTM spin up on, 0 = NSSTM spin up off
!< nstf_name(3) : 1 = NSST analysis on, 0 = NSSTM analysis off
!< nstf_name(4) : zsea1 in mm
!< nstf_name(5) : zsea2 in mm

## Slide 21
Surface temperature=302.15 K @ hour 0.5
Land_Sea_Ice_mask=0 @ hour 0.5
Test No.IV / 57a

## Slide 22
@0.5 hrs
@120 hrs
@240 hrs
Test No.IV / 57a
Surface Pressure

## Slide 23
@0.5 hrs
@120 hrs
@240 hrs
Test No.IV / 57a
U at 10m

## Slide 24
@0.5 hrs
@120 hrs
@240 hrs
Test No.IV / 57a
V at 10m

## Slide 25
Chart: Sea Level Pressure (Test No.IV)
| 0 | 6 | 12 | 18 | 24 | 30 | 36 | 42 | 48 | 54 | 60 | 66 | 72 | 78 | 84 | 90 | 96 | 102 | 108 | 114 | 120 | 126 | 132 | 138 | 144 | 150 | 156 | 162 | 168 | 174 | 180 | 186 | 192 | 198 | 204 | 210 | 216 | 222 | 228 | 234 | 240
 | 1004.4414 | 1004.7134 | 1004.0821 | 1004.3333 | 1006.6336 | 1005.162 | 1004.6426 | 1001.7444 | 998.624 | 989.5532 | 977.3652 | 964.3353 | 975.9278 | 971.8823 | 975.1114 | 983.3858 | 987.3522 | 978.33 | 970.7802 | 975.2135 | 986.787 | 979.2851 | 969.8014 | 975.6083 | 977.754 | 976.2238 | 959.9959 | 958.6205 | 964.3318 | 936.9181 | 930.6724 | 953.0449 | 944.6364 | 945.1095 | 944.8766 | 939.4784 | 951.3411 | 948.2568 | 943.6672 | 942.4298 | 948.387
Test No.IV / 57a SLP forecast
Forecast hours

## Slide 26
HOW TO RUN
(1) Download the code
https://github.com/ufs-community/ufs-weather-model/wiki
% git clone https://github.com/ufs-community/ufs-weather-model
(2) Build
https://ufs-weather-model.readthedocs.io/en/ufs-v1.0.0/ContributingDevelopment.html (3.3.1 /3.3.3)
cd ./modulefiles/hera.intel
module use . ---- module load fv3 ---- ./build.sh
(3) simple-test-case
https://github.com/ufs-community/ufs-weather-model/wiki/Getting-Started (3 /4 )
% wget https://ftp.emc.ncep.noaa.gov/EIB/UFS/simple-test-case.tar.gz
(4) input.nml .... changed
&test_case_nml ---- added ------
test_case = -55
bubble_do = .false.
alpha = 0.
Nsolitons = 1
soliton_size = 750.e3,
soliton_Umax = 50. /
external_ic = .false. ---- changed as "false"
external_eta = .false.
(5) Submit your job and relax

## Slide 27
./ufs-weather-model/FV3/io/FV3GFS_io.F90
!--- 2D variables
! ------------
Sfcprop(nb)%slmsk(ix) = sfc_var2(i,j,1) !--- slmsk
Sfcprop(nb)%tsfco(ix) = sfc_var2(i,j,2) !--- tsfc (tsea in sfc file)
Sfcprop(nb)%weasd(ix) = sfc_var2(i,j,3) !--- weasd (sheleg in sfc file)
Sfcprop(nb)%tg3(ix) = sfc_var2(i,j,4) !--- tg3
Sfcprop(nb)%zorlo(ix) = sfc_var2(i,j,5) !--- zorl on ocean
Sfcprop(nb)%alvsf(ix) = sfc_var2(i,j,6) !--- alvsf
Sfcprop(nb)%alvwf(ix) = sfc_var2(i,j,7) !--- alvwf
Sfcprop(nb)%alnsf(ix) = sfc_var2(i,j,8) !--- alnsf
Sfcprop(nb)%alnwf(ix) = sfc_var2(i,j,9) !--- alnwf
Sfcprop(nb)%facsf(ix) = sfc_var2(i,j,10) !--- facsf
Sfcprop(nb)%facwf(ix) = sfc_var2(i,j,11) !--- facwf
Sfcprop(nb)%vfrac(ix) = sfc_var2(i,j,12) !--- vfrac
Sfcprop(nb)%canopy(ix) = sfc_var2(i,j,13) !--- canopy
Sfcprop(nb)%f10m(ix) = sfc_var2(i,j,14) !--- f10m
Sfcprop(nb)%t2m(ix) = sfc_var2(i,j,15) !--- t2m
0: NOTE from PE 0: reading surface properties data from INPUT/sfc_data.tile*.nc
Code modification

## Slide 28
Sfcprop(nb)%q2m(ix) = sfc_var2(i,j,16) !--- q2m
Sfcprop(nb)%vtype(ix) = sfc_var2(i,j,17) !--- vtype
Sfcprop(nb)%stype(ix) = sfc_var2(i,j,18) !--- stype
Sfcprop(nb)%uustar(ix) = sfc_var2(i,j,19) !--- uustar
Sfcprop(nb)%ffmm(ix) = sfc_var2(i,j,20) !--- ffmm
Sfcprop(nb)%ffhh(ix) = sfc_var2(i,j,21) !--- ffhh
Sfcprop(nb)%hice(ix) = sfc_var2(i,j,22) !--- hice
Sfcprop(nb)%fice(ix) = sfc_var2(i,j,23) !--- fice
Sfcprop(nb)%tisfc(ix) = sfc_var2(i,j,24) !--- tisfc
Sfcprop(nb)%tprcp(ix) = sfc_var2(i,j,25) !--- tprcp
Sfcprop(nb)%srflag(ix) = sfc_var2(i,j,26) !--- srflag
Sfcprop(nb)%snowd(ix) = sfc_var2(i,j,27) !--- snowd (snwdph in the file)
Sfcprop(nb)%shdmin(ix) = sfc_var2(i,j,28) !--- shdmin
Sfcprop(nb)%shdmax(ix) = sfc_var2(i,j,29) !--- shdmax
Sfcprop(nb)%slope(ix) = sfc_var2(i,j,30) !--- slope
Sfcprop(nb)%snoalb(ix) = sfc_var2(i,j,31) !--- snoalb
Sfcprop(nb)%sncovr(ix) = sfc_var2(i,j,32) !--- sncovr
if(Model%cplflx) then
Sfcprop(nb)%tsfcl(ix) = sfc_var2(i,j,33) !--- sfcl (temp on land portion of a cell)
Sfcprop(nb)%zorll(ix) = sfc_var2(i,j,34) !--- zorll (zorl on land portion of a cell)
end if
Code modification

## Slide 29
./ufs-weather-model/FV3/io/FV3GFS_io.F90
./ufs-weather-model/FV3/gfsphysics/physics/sfcsub.F
#ifdef TC_AQUA
------------------------------------------------
#else
------------------------------------------------
#endif
#ifndef TC_AQUA
------------------------------------------------
#else
------------------------------------------------
#endif
So far, two codes need to be modified for TC_AQUA, and more changes for FV3GFS shallow water model.
#ifdef SW_DYNAMICS
------------------------------------------------
#else
------------------------------------------------
#endif
#ifndef SW_DYNAMICS
------------------------------------------------
#else
------------------------------------------------
#endif

## Slide 30
Test No.V (test_case= 4a/b) with FV3GFS shallow-water model
ubar = 50. (m/s) ! maxmium wind speed
r0 = 250.e3 (m) ! RADIUS of the maximum wind of the Rankine vortex
(4b)ddeg = 3.*r0/radius ! Distance between the Two-vortices (6.7 degree*2.0)
p1(1) = pi*1.75 – ddeg ! 45W -ddeg
p1(2) = pi/6. ! 30 N
call rankine_vortex(ubar, r0, p1, u, v, grid, bd)
p2(1) = pi*1.75 + ddeg ! 45W +ddeg
p2(2) = pi/6. ! 30 N
call rankine_vortex(ubar, r0, p2, u, v, grid, bd)
if( r<r0 ) then
vr = ubar*r/r0
else
vr = ubar*r0/r
endif
(4a)ddeg = 6.*r0/radius ! Distance between the Two-vortices (13.4 degree*2.0)

## Slide 31
@001 hr
@120 hrs
@060 hrs
@024 hrs

## Slide 32
@001 hr
@024 hrs
@060 hrs
@120 hrs

## Slide 33: Questions and suggestions ????
Summary:
the 2D/3D idealized TC could be run under FV3-GFS V15/16 framework.
Applications:
it could be a platform for the investigation of TC basic dynamics and physics as well.
Goal: this platform will be built on global 9Km/3Km resolution.
Hope: quantum computer is on the way!
C48 = 2­degree, C96=1­degree, C192 = 0.5­degree ≈ 50km, C384 = 0.25­degree ≈ 25km, C2560 ≈ 3.5km)

## Slide 34: Questions and discussion: GFS-V15/16 has large cross-track bias, why?