## Slide 1: Dispersion Modeling Support at the NOAA /NWS National Centers for Environmental Prediction (NCEP) and OAR/Air Resources Lab (ARL)
Jeff McQueen, Geoff DiMego,
Caterina Tassone, Marina Tsidulko, Binbin Zhou,
Yanqui Zhu, Sarah Lu, Ho-Chun Huang and Geoff Manikin
(NCEP/EMC)
Roland Draxler, Barbara Stunder and Glenn Rolph
(NOAA/ARL)
July 12, 2011

## Slide 2: Progress with Operational Meteorological and Dispersion Model Support
Progress towards:
  WMO Regional Specialized Meteorological Center support
    Run at NCEP 24/7 by Senior Duty Met (SDM)
  Homeland Security support
    1.3 km nest
  Volcanic Ash, dust, smoke global capability
Probabilistic Prediction
  High Resolution Meteorological Ensembles
Evaluation Techniques
  Concentration Evaluation
Future Directions

## Slide 3: NOAA’s Model Production Suite
WRF NMM/ARW
Workstation WRF
Chesapeake
Tampa
Delaware
ADCIRC
Air Quality
WRF: ARW, NMM
ETA, RSM
GFS, Canadian Global Model
Regional NAM
NEMS NMM
North American Ensemble Forecast System
Hurricane GFDL
HWRF
Global
Forecast
System
Dispersion
ARL/HYSPLIT RSMC, Volc Ash
Forecast
Severe Weather
Rapid Update
for Aviation
Climate
CFSv2
Short-Range
Ensemble Forecast
MOM4
NOAH Land Surface Model
Coupled
Global Data
Assimilation
Oceans
HYCOM
WAVEWATCH III
NAM/CMAQ, smoke, dust
3
Regional
DA
Regional
DA
Satellites + Radar
99.9%
3.5B Obs/Day
NOS
PORTS
GLOFS

## Slide 4
NEMS Component Structure
MAIN
EARTH(1:NM)
Ocean
Atm
Ice
Below the dashed line, the source codes are organized by the model developers.
FIM
Dyn
Phy
Wrt
NEMS
Ensemble
Coupler
GFS
Dyn
Phy
Wrt
NMM
Dyn
Phy
Nest Domains(1:ND)
Wrt
All boxes represent
ESMF components.
NEMS
LAYER
ARW
Dyn
Phy
Wrt
WRFChem
GOCART
CMAQ

## Slide 5
National Environmental Modeling System FY11; Q3
12 km
4 km
6 km
3 km
3 km
1.5 km
1.33 km
Nonhydrostatic Mesoscale Model (NMM)  NonHydrostatic Multiscale Model on B grid (NMMB)
-- Physics retuned for NMMB
-- Additional data sets: Windsat, ASCAT, ACARS humidity, NOAA-19 (HIRS and AMSU-A), IASI radiances, AQUA (AMSU-A), GPS (radio occultation)
Parent (12 km)
– 84 hrs
Children (6, 4 & 3 km)
– 60 hrs
IMET (1.5 & 1.33 km)
– 36 hrs

## Slide 6
19Z 11 August
Tropical Depression 5
1000 m REFD, 10 m winds
NCEP Test of Fire Wx Nest Capability Gulf Spill 1.33 km NEMS/NMMB nest

## Slide 7: Google Map of 4 RTMA Domains First Phase of Analysis of Record
Real Time Mesoscale Analysis
Analyzed every hour on the NWS’ NDFD grids
10 m wind + est. anal. uncertainty
2m Temperature + est.anal.unc.
2m dew point + est.anal.unc.
Sfc pressure + est.anal.uncertainty
1 hr precip (Stage 2)
GOES Eff. Cloud Amount, PBLH
Courtesy of Yan Zheng University of Utah

## Slide 8
Operational HYSPLIT
  Volcano, RSMC, Homeland Security
HLS

## Slide 9
IAEA Long Range Transport Plume
New York Times March 16, 2011
JMA estimate

## Slide 10
Archive of NOAA experimental tracer data and meteorology is on-line and in a common data format
Meteorology comes primarily from the regional reanalysis
WEB directory also includes all statistical programs, and the …
model configuration used to produce tabulated results
Evaluation Techniques
Comparison to experimental data
http://www.arl.noaa.gov/DATEM.php

## Slide 11
http://www.arl.noaa.gov/DATEM_results.php
EXPERIMENT | Average | Paired
ACURATE (18 m) | 3.25 | 1.77
ANATEX (33) | 3.48 | 1.84
ANATEX (33) | 2.66 | 1.63
CAPTEX (6) | 3.24 | 1.63
1ETEX (1) | 2.37 | 1.55
1INEL74 (2 m) | 1.71 | 1.37
METREX (243) | 2.81 | 1.77
METREX (243) | 2.27 | 1.58
OKC80 (2) | 2.50 | 1.73
North American Regional Reanalysis: http://nomads.ncdc.noaa.gov
11
Comparison to experimental data, cont’d

## Slide 12
June-July reliability
Lower dosage show good reliability
Higher dosage has positive bias over higher probability range
Aug-Sept-Oct Reliability
Overwhelmingly large positive bias over high probability range
Probabilistic verification
Reliability Diagram – indicates joint bias
4 km MM5 Analysis SCIPUFF “Truth” vs
32 km SREF SCIPUFF Forecast

## Slide 13
Economic Value (EV)
Performance over different cost/loss ratio
High dosage prediction over low cost/ratio has high EV.
Answer such questions as:
If cost/loss is extremely low, e.g. loss is so high that cost can be neglected, then take action in lower probability has skill?
The answer is YES, according to EV
Lower probability means higher FAR
(don’t care false alarm to take action)
For high, less dangerous dosage, should use moderate prob thresholds
Low prob High prob

## Slide 14: Hybrid High Resolution Ensemble Prediction
High Resolution Model | Domain | Resolution | Time lagged members | # members
NAM NEMS NMMB nest | CONUS | 4 km/L35 | Current, T-6, T-12h | 3
NOAA/ ESRL HRRR | CONUS | 3 km/L35 | Current, T-1, T-2, T-3, T-4, T-5, T-6 | 7
WRF High Resolution Window ARW | Eastern U.S. Western U.S. | 4.5 km/L35 | Current, T-12 | 2
WRF High Resolution Window NMM | Eastern U.S. Western U.S. | 4 km/L35 | Current, T-12 | 2
NEMS/NMMB Storm Prediction Center (SPC) Configuration | CONUS | 4 km/L35 | Current, T-12 | 2

## Slide 15: Inline Tracer Development courtesy of Youhua Tang
NMM-B tracer run with initial cuboid-shaped field
Regional NMM-B with 3-D tracer advection (no tracer physics & diffusion)
Tracer initialized at center of the domain from bottom to top (cuboid form)
Zero lateral boundary conditions
500 hPa field shown

## Slide 16: Global Dispersion Modeling
Executable compiled from NEMS trunk code repository
120-hr dust-only forecast
Once per day (00Z)
3-hourly products: 3d distribution of dust aerosols (5 bins from 0.1 – 10 µm)
Automatic output archive, post processing and web update since June 11, 2011
Same physics and dynamics as operational GFS with the following exceptions:
  Lower resolution (T126 L64)
  Use RAS with convective transport and tracer scavenging
  Aerosol-radiation feedback is turned off
Experimental (non-operational)

## Slide 17
NASA GPS RO (COSMIC) data
+ Sonde/ACARS data
+MPLNET lidar + NexRad data
Boundary Layer Analysis
Verification:
Calipso products
NCAS lidar, ESRL Profilers
National PBL Products

## Slide 18: Improved Boundary Layer Analysis
Cap PBL Profilers
MPLNET Lidars
Need more observations for analysis to have an impact
Need more independent observations for verification

## Slide 19: Lessons Learned & Recommendations
Need for NRT relocatable, global operational high resolution NWP – Atmospheric Dispersion modeling capability w/ data assimilation
  WMO/RSMC  Most useful for long rang transport (GFS-HYSPLIT)
  NMCs coordination thru RSMC process (information thru secure web pages)
    Better coordination with non-NMC centers (eg: DOE, DOD…)
    Better define & interpret model output strengths/weaknesss (long range vs near-field products)
Enhance boundary layer measurements for evaluation, assimilation:
  Radiosondes, field experiments, ACARS
  PBL Profilers (e.g.: U.S., Japan, Europe)
  Lidar (EARLINET, WMO- GALION), ASOS Ceilometers (PBLH, Aerosols)
  Develop boundary layer reanalysis (downscale NARR, ERA ?)
Develop and evaluate high resolution ensemble met systems
  HRRR, Time Lagging, Composite
  Include boundary layer uncertainty, new metrics
  Additional products: threshold probabilities, Plume time of arrival
Evaluate in-line dispersion within NWP modeling techniques
  Esp for aerosol interactions w radiation/clouds (smoke, dust, ash)